## Slide 1
Universidad Politécnica de Cartagena
Nonlinear Finite Element Analysis of Mooring Cables on Marine Structures
Gutiérrez-Romero, JE. García-Espinosa, J. Zamora-Parra, B. Esteve-Pérez JA.
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
COMPASS
WWW.COMPASSIS.COM

## Slide 2
Index
Introduction
Problem statement
Approach to coupling algorithm
Analysis examples
Conclusions
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy

## Slide 3
1
Introduction
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy

## Slide 4
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
Development of Deep water technology
Shallow water
Deep water
1. Introduction
Main challenges of offshore industry/renewable energies are
Harsh environment
Offshore wind market expansion
Mooring and risers
Variety of platforms

## Slide 5
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
1. Introduction
Marine cable structures has reached great interest
Wide range of application
Great importance in offshore production system
Classical solutions give unrealistic solution
Cable solutions approach has been compared:
  Linear spring
  Nonlinear spring
  Quasi-static solution
  FEM solution
  Nonlinear FEM solution
Coupling floater dynamics with environmental loads and external loads may be considered as key in realistic simulations.
Authors presents in this work an application to couple NFEM cable model with second - order wave and wind loads.
Nonlinear wave loads
Nonlinear mooring loads
Nonlinear wind loads

## Slide 6
2
Problem statement
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy

## Slide 7
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
2. Problem statement
Cable dynamics:
Most cases, the bending and the torsion effects are negligible. The set of last equations can be formulated as
The mathematical model considers:
Self weight
Hydrostatics loads
Drag loads
Viscous loads
Seabed interaction
Geometric nonlinearities

## Slide 8
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
2. Problem statement
Spatial discretization of cable element. Time integration
Applying FEM on current configuration of cable element the balance of momentum can be formulated as
The dynamic equilibrium in current configuration of an element can be written:
Time integration using Bossak-Newmark scheme
Aitken acceleration method

## Slide 9
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
2. Problem statement
Seakeeping solver. SeaFEM
1st and 2nd Stokes regular and spectral waves, including user
defined spectrum. 1st and 2nd solution can be decomposed on:
  Incident wave potential and diffraction - radiation velocity potential
  Incident wave elevation and diffraction –radiation wave elevation
Solve using FEM on unstructured meshes
Real forward speed with Streamline & SPUG integration
GPU computing
Hydro-elasticity solver for strength and fatigue assessment
Seakeeping solver based on previous work of García-Espinosa and Serván-Camas.
SeaFEM includes state-of-the-art radiation and diffraction BEM and FEM solvers, enabling frequency domain and direct time-domain analyses of the dynamic response of the structure.

## Slide 10
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
3
Coupling rigid body motions & external loads

## Slide 11
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
2. Coupling Rigid body motion & external loads
Once the velocity potential has been estimated in the current time step, a loop to determine the dynamics of floater is launched.
Then, the pressure on the wetted surface of the floating device is calculated and the different external forces and moments acting on the floater are evaluated.
The new position of the floater for the l-iteration of the iterative loop is obtained adding the restoring force vector of mooring cables.
The fairlead position of the cable is updated. Then, the dynamics of cable is calculated. The stiffness matrix of the different lines is evaluated by numerical differentiation. For every l-iteration of the floater dynamics loop, the restoring mooring forces are evaluated.
A new l+1+iteration from step 2 to 5 is carried out, until the convergence of the floater dynamics loop is reached.
Once the floater dynamics obtaining has converged, a new k+1-iteration of the velocity potential loop is done until convergence. When the convergence of this loop has been achieved, a new time step solution is initiated.
Update:
No
Convergence:
No
Yes
Calculus: ;
Body dynamics loop (l)
Solver loop (k)
Time-marching loop (n)
Solve:
Convergence:
Calculate:
Yes

## Slide 12
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4
Application examples

## Slide 13
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples

## Slide 14
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
GVA platform analysis
Main particulars: | 
Displacement (ton) | 25940
Center of gravity above keel (m) | 21.35
Radii of inertia Rxx (m) | 30.40
Radii of inertia Ryy (m) | 31.06
Radii of inertia Rzz (m) | 37.54
RAO validation

## Slide 15
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
GVA 4000 platform analysis
Wave spectrum: JONSWAP
Peak period: 7.7 s
Significant wave height: 3.0 m
Number of mooring lines: 8
Stiffness: 3.84x107 N
Length of lines: 520.0 m
Weight per unit length: 698.1 N/m
Nº of elements/line: 100
 | Surge (m) | Sway (m) | Heave (m) | Roll (º) | Pitch (º) | Yaw (º)
Mean 1st | -0.01 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Mean 2nd | 0.55 | 0.01 | 0.01 | 0.06 | 0.06 | -0.03
Amplitude 1st | 1.20 | 0.12 | 1.44 | 0.39 | 1.37 | 0.17
Amplitude 2nd | 4.87 | 0.59 | 1.48 | 2.19 | 2.09 | 0.80
RMS 1st | 0.17 | 0.02 | 0.21 | 0.07 | 0.22 | 0.03
RMS 2nd | 1.10 | 0.10 | 0.21 | 0.37 | 0.36 | 0.16
Low amplitude of heave motion
Low amplitude rotations

## Slide 16
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
GVA 4000 platform analysis
Mooring tensions ≈ line weight
In general, good response in operating conditions
But noticeable peaks are identified in the time series …
 | Max. (105 N) | Min. (105 N) | Mean (105 N) | RMS (105 N)
Line 1 | 4.309 | 3.930 | 4.118 | 4.119
Line 2 | 4.308 | 3.908 | 4.117 | 4.118
Line 3 | 4.305 | 3.922 | 4.118 | 4.118
Line 4 | 4.3195 | 3.934 | 4.118 | 4.119

## Slide 17
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
Spar OC3 fully analysis
Main particulars: | 
Displacement (ton) | 8163.76
Center of gravity below SWL (m) | -75.098
Radii of inertia Rxx (m) | 49.41
Radii of inertia Ryy (m) | 49.48
Radii of inertia Rzz (m) | 5.64
RAO validation

## Slide 18
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
Spar OC3 fully analysis
Wind turbine: Linearized model (operating condition). FASTLognoter
Wind profile: coupling with AeroDyn (time history loads)
Waves: FEM hydrodynamics model
(1st & 2nd ) + JONSWAP spectrum
Mooring: Nonlinear FEM cable model
Time – Domain Analysis
Wave spectrum: JONSWAP
Peak period: 12 s
Significant wave height: 6.0 m
Mean Wind velocity: 11.4 m
Number of mooring lines: 3
Stiffness: 6.04x1010 N
Length of lines: 902 m
Weight per unit length: 698.1 N/m
Nº of elements/line: 200
Wind Loads

## Slide 19
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
Spar OC3 fully analysis
 | Surge (m) | Sway (m) | Heave (m) | Roll (º) | Pitch (º) | Yaw (º)
Mean 1st | -0.01 | 0.00 | -0.01 | 0.29 | 0.40 | 0.21
Mean 2nd | 0.10 | 0.00 | -0.03 | 0.30 | 0.42 | 0.28
Amplitude 1st | 13.82 | 1.12 | 2.61 | 1.92 | 6.03 | 10.31
Amplitude 2nd | 15.19 | 1.55 | 2.59 | 2.02 | 8.00 | 10.83
RMS 1st | 2.54 | 0.18 | 0.50 | 0.52 | 1.09 | 1.09
RMS 2nd | 2.73 | 0.24 | 0.45 | 0.48 | 1.22 | 1.91
Similar trends between First and Second-Order wave environment
Higher amplitudes on pitch motion
Excursions on surge

## Slide 20
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
Spar OC3 fully analysis
 | Max. (106 N) | Min. (106 N) | Mean (106 N) | RMS (106 N)
Line 1 | 1.457 | 1.052 | 1.246 | 1.248
Line 2 | 1.471 | 1.040 | 1.236 | 1.238
Line 3 | 0.742 | 0.451 | 0.593 | 0.954
One line supports main environmental loads
Good performance in operational conditions

## Slide 21
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
Semisubmersible OC4 fully analysis
Main particulars: | 
Displacement (ton) | 13473
Center of gravity below SWL (m) | -9.205
Radii of inertia Rxx (m) | 29.21
Radii of inertia Ryy (m) | 29.21
Radii of inertia Rzz (m) | 30.59
RAO analysis

## Slide 22
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
Wind turbine: Linearized model (operating condition). FASTLognoter
Wind profile: coupling with AeroDyn (time history loads)
Waves: FEM hydrodynamics model
(1st & 2nd ) + JONSWAP spectrum
Mooring: Nonlinear FEM cable model
Time – Domain Analysis
Wave spectrum: JONSWAP
Peak period: 12 s
Significant wave height: 6.0 m
Mean Wind velocity: 11.4 m
Number of mooring lines: 3
Stiffness: 1.63x1011 N
Length of lines: 835.5 m
Weight per unit length: 1066.0 N/m
Nº of elements/line: 200
Semisubmersible OC4 fully analysis
Wind Loads

## Slide 23
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
 | Surge (m) | Sway (m) | Heave (m) | Roll (rad) | Pitch (rad) | Yaw (rad)
Mean 1st | -0.34 | -0.71 | 0.22 | 0.01 | 0.10 | 0.00
Mean 2nd | -0.19 | -0.72 | 0.08 | 0.01 | 0.10 | 0.00
Amplitude 1st | 7.10 | 1.21 | 3.86 | 0.01 | 0.12 | 0.01
Amplitude 2nd | 6.81 | 1.22 | 3.89 | 0.01 | 0.12 | 0.01
RMS 1st | 1.40 | 0.75 | 0.90 | 0.01 | 0.10 | 0.00
RMS 2nd | 1.33 | 0.76 | 0.88 | 0.01 | 0.10 | 0.00
Similar trends between First and Second-Order wave environment
Higher amplitudes on pitch motion
Excursions on surge
Semisubmersible OC4 fully analysis

## Slide 24
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
4. Application examples
 | Max. (106 N) | Min. (106 N) | Mean (106 N) | RMS (106 N)
Line 1 | 1.522 | 1.198 | 1.884 | 1.526
Line 2 | 0.823 | 0.775 | 0.880 | 0.823
Line 3 | 0.864 | 0.813 | 0.930 | 0.864
One line supports main environmental loads
Good performance in operational conditions
Semisubmersible OC4 fully analysis

## Slide 25
5
Conclusions
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy

## Slide 26
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
5. Conclusions
Seakeeping model for solving the governing equations for second-order wave diffraction-radiation problem.
An introduction to cable dynamic formulation has been described.
Formulation based on Nonlinear FEM dynamic cable model to solve realistic problems has been presented.
A scheme for the fully coupled analysis of a floating structure and nonlinear external loads.
Fully coupled formulation to determine the dynamic behaviour of three representative examples of offshore structures has been performed.

## Slide 27
Universidad Politécnica de Cartagena
Thanks for your attention!
VI International Conference on
Computational Methods in Marine Engineering
Marine 2015
15 -17 June 2015, Rome Italy
COMPASS
WWW.COMPASSIS.COM
Nonlinear Finite Element Analysis of Mooring Cables on Marine Structures
Corresponding Author:
jose.gutierrez@upct.es